| Canadian Natural Resources Limited GENERAL PRESSURE VESSEL INFORMATION Job 10.112800 |
| --- |
| District: Hinton | Skid No. |
| Facility: Wild River West | Location (LSD): 08-30-57-24 W5M |
| Vessel Name Equipment Number: Glycol Contactor |
| Orientation: Vertical |
| Status: Out-of-Service |  |
| PRESSURE VESSEL NAMEPLATE DATA |
| “A” or “G” or “S” (Sask.) or BC Registration Number. A0490017 | CRN Number: P9234.2 |
| Vessel serial number: C1749A.C | Size: 24” x 40’ |
| Shell thickness: | Shell material: SA-516-70 N |
| Head thickness: | Head material: SA-516-70N |
| Tube wall thickness: | Tube material: |
| Tube diameter: | Tube length: |
| Channel thickness: | Channel material: |
| Design pressure | Shell: 12411 KPag | Operating pressure | Shell: |
|  | Tubes: |  | Tubes: |
| Design Temp. | Shell: 66℃ | Operating temperature | Shell: |
|  | Tubes: |  | Tubes: |
| X-ray: RT-2 | Heat treatment: No |
| Code parameters: ASME section 8 Division 1 | Coated: Not stated. |
| Manufacturer: Rushton | Year built: 2002 |
| Corrosion allowance: Nil | Manway: No |
| PRESSURE SAFETY VALVE NAMEPLATE DATA |
| PSV Tag # | Manufacture / Model / Serial | Set Pressure (PSI / kPa) | Capacity (scfm) | Size | Block Valve | Location | Service by Date |
| CFOL 2926 | Taylor / 82E8351311 / 1272-1 | 1420 psi | 5110 scfm | 1x1 | No | Shell | Wizard 23-7-2012 |
| SERVICE CONDITIONS-INDICATE ALL THAT APPLY |
| Sweet X | Sour | Oil | Gas X | Water |
| Amine | LPG | Condensate | Air | Glycol X |
| Other (Describe): |

# Inspection Interval ________________________________________PSV Service Interval_________________________________

# (Determined by MIC in conjunction with Chief Inspector following guidelines of CNRL’s Owner-User Inspection Program)

Reports reviewed and accepted by:

# Mechanical Integrity Coordinator________________________________________________Date__________________________

# Fill out all forms as completely as possible. All information is important!  Use back of sheets to record additional information or sketch if required.

# Copy of report to be filed by MIC at site, and copy sent to Chief Inspector

Inspected By:	Keith Kowal (ABSA 0414)		                                                                         Date: 27 February 2013

| LSD | Burner Data Plate |
| --- | --- |
| Vessel overview | PSV |
| PSV. | PSV service tag. |