| Canadian Natural Resources Limited GENERAL PRESSURE VESSEL INFORMATION Job # 10.110194 |
| --- |
| District: Fort St John, BC | Skid No. |
| Facility: Inga Compressor Station | Location (LSD): 05-21-88-23-W6M |
| Vessel Name Equipment Number: Flare Knock Out Drum |
| Orientation: Horizontal |
| Status: In Service | Regulatory Inspection |
| PRESSURE VESSEL NAMEPLATE DATA |
| “A” or “G” or “S” (Sask.) or BC Registration Number. C46059 | CRN Number: N-7030.21 |
| Vessel serial number: 97-8998-1 | Size: 60 in x 15 ft |
| Shell thickness: 9.5 mm | Shell material: SA-516-70 |
| Head thickness: 8.7 mm | Head material: SA-516-70 |
| Tube wall thickness: | Tube material: |
| Tube diameter: | Tube length: |
| Channel thickness: | Channel material: |
| Design pressure | Shell: 345Kpa | Operating pressure | Shell: |
|  | Tubes: |  | Tubes: |
| Design Temp. | Shell: 66 deg C | Operating temperature | Shell: |
|  | Tubes: |  | Tubes: |
| X-ray: RT-1 | Heat treatment: Nil |
| Code parameters: ASME Sec VIII, DIV 1 | Coated: No |
| Manufacturer: Wells – Hall Fabrication Ltd. | Built: 1997 |
| Corrosion allowance: N/S | Manway: No |
| PRESSURE SAFETY VALVE NAMEPLATE DATA |
| PSV Tag # | Manufacture | Model # | Serial # | Set Pressure (Kpa) | Capacity (scfm) | Service Date |
|  |  |  | No access to PSV |  |  |  |
| CRN # | Service By | Block Valve | Location | Size | Code Stamp |  |
| SERVICE CONDITIONS-INDICATE ALL THAT APPLY |
| Sweet | Sour X | Oil X | Gas X | Water X |
| Amine | LPG | Condensate X | Air | Glycol |
| Other (Describe): |

# Inspection Interval ________________________________________PSV Service Interval_________________________________

# (Determined by MIC in conjunction with Chief Inspector following guidelines of CNRL’s Owner-User Inspection Program)

Reports reviewed and accepted by:

# Mechanical Integrity Coordinator________________________________________________Date__________________________

# Fill out all forms as completely as possible. All information is important!  Use back of sheets to record additional information or sketch if required.

# Copy of report to be filed by MIC at site, and copy sent to Chief Inspector

| External Inspection Items | G | F | P | N/A | Comments |
| --- | --- | --- | --- | --- | --- |
| Insulation Verify sealed around manways, nozzles, no damage present, and there is no egress of moisture. | X |  |  |  | Vessel is 100% insulated, as best effort the insulation is in good overall condition no visible signs of mechanical damage or moisture egress detected. |
| External Condition Assess paint condition, areas peeling, record any corrosion, damage, etc (record location, size and depth of corrosion or damage) |  |  |  | X | Vessel is fully insulated. |
| Leakage Record any leakage at flanges, threaded joints, weep holes on repads, etc. | X |  |  |  | No leaking detected. |
| Saddle Assess condition of paint, fire protection, and concrete. Look for corrosion, buckling, dents, etc. Look at vessel surface area near supports. Verify no signs of leakage at attachment to vessel and attachment welds are acceptable. Ground wire attached? | X |  |  |  | Saddles are in good condition – no buckles or distortion. Paint intact – with no visible corrosion. Vessel grounded at the skid. |
| Anchor Bolts Hammer tap to ensure secure. Look for cracking in treads or signs of deformation. | X |  |  |  | Vessel is firmly bolted to skid floor. |
| Concrete foundation Check for cracks, spalling, etc. |  |  |  | X | None. |
| Ladder / Platform Describe general condition, ensure support is secure to vessel, and describe any hazards. |  |  |  | X | None. |
| Nozzle Assess paint, look for leakage, and ensure stud threads are fully engaged. Record any damage, deflection, etc. Are nozzles gusseted? | X |  |  |  | All threads connections fully engaged. No deflection – no leaks. Paint in good condition. Nozzles are not gusseted. |
| Gauges Ensure gauges are visible, working, no leakage, and suitable for range of MAWP/ Temp. |  |  |  | X | No Pressure gauge. No Temperature. |
| External Piping Ensure pipe is well supported. All clamps, supports, shoes, etc. in place. Look for evidence of structural overload, deflection, etc. Paint condition, external corrosion? | X |  |  |  | Well supported – no deflection – all clamps and shoes in place. Piping is insulated & appears to be in good condition – no visible mechanical damage noted. |
| Valving Ensure no leaks are visible. Valves are properly supported and chained if necessary. | X |  |  |  | Well supported – no leaks. |
| PSV Ensure PSV is set at pressure at or below that of vessel. | X |  |  |  | Located on inlet piping – Unable to access the PSV to determine set pressure. Discharge piping is the same size as the outlet to PSV. No block valve present. PSV vents to flare. |
| NDE methods Was UT/ MPI done on vessel (MI coordinator to review results) | X |  |  |  | Ultrasonic thickness survey carried out-no metal thickness detected below nominal. |
| Recommendations or corrective actions : Vessel is Fit for Service or describe corrective actions required) (MIC to review corrective actions with Operations, discuss with Chief Inspector where necessary, and get remedial action implemented) Recommendations: 1. No recommendations at this time. Summary: This vessel is in good over all condition, visual external and ultrasonic thickness survey carried out – no metal thickness detected below nominal. Long term corrosion rate based on greatest thickness loss – no corrosion rate to assess. Vessel is fit for service. |

Inspected By: Joseph Holdstock						                                              Date: April 15, 2011.

| LSD Location | Site overview |
| --- | --- |
| Data plate | Vessel Overview |
| PSV location – no access |  |