| CNRL Business District (e.g. NE Gas, St. Albert, Bonnyville, Edson) | GRANDE PRAIRIE | MT # (from attached blank MT) |  |
| --- | --- | --- | --- |
|  |  | Date of Insp. | 5/16/2012 |
| Prov. Reg.# (e.g. A#. RAE#, C#) | A0446637 | Location (Field Name) | CHIN NORTH RUN, CRANBERRY |
| Equipment Type (e.g. treater, separator, scrubber) | CONTACTOR | LSD | 08-13-097-04W6 |
|  |  | Previous LSD |  |
| Tag/Equip. # (e.g. V-101) |  | Comp./Unit # (e.g. 1408) |  |
| Vessel Status: | In Service | Not In Service X | Job # |  |
| Fabricator | RUSHTON GAS & OIL | Serial # | C847A.C | MAWP/Temp | 9929 KPA 54 C |
| CRN# | L0595.123 | Shell Mat’l |  | Shell Thick. |  |
| Corr. All. |  | Head Mat’l |  | Head Thick. |  |
| Diameter | 2 FT | Length |  | Height | 26 FT | RT |  | HT |  |
| Year Built | 1998 | Next Insp. |  | Insp. Type |  |
| Service | SWEET | Manway | N | Coating |  |
| PSV #. |  |
| Mfg. | TAYLOR | Serial # | 61162-209 | Set Pressure | 1440 PSI |
| Type/Model | T-8200-2 | Capacity | 307m3 | Size | 2 |
| Date of Service | 11/1998 | Next Service |  | Service Co. | D.V. METER |

Notes:												Report #

Completed by: Don Burren				Contact Number: 403-304-4951