| CNRL Business District (e.g. NE Gas, St. Albert, Bonnyville, Edson) | GRANDE PRAIRIE | MT # (from attached blank MT) |  |
| --- | --- | --- | --- |
|  |  | Date of Insp. | 5/16/2012 |
| Prov. Reg.# (e.g. A#. RAE#, C#) | A2910415 | Location (Field Name) | CHIN NORTH RUN, CRANBERRY |
| Equipment Type (e.g. treater, separator, scrubber) | 3 PHASE SEPARATOR | LSD | 05-17-097-03W6 |
|  |  | Previous LSD |  |
| Tag/Equip. # (e.g. V-101) |  | Comp./Unit # (e.g. 1408) |  |
| Vessel Status: | In Service X | Not In Service | Job # |  |
| Fabricator | ALCO GAS & OIL | Serial # | 93C-5003-01B | MAWP/Temp | 1330 PSI 250 F |
| CRN# | K6916.2 | Shell Mat’l | SA-516-70 | Shell Thick. | 0.75 |
| Corr. All. |  | Head Mat’l | SA-516-70 | Head Thick. | 0.837 |
| Diameter | 1.75 FT | Length |  | Height | 7.5 FT | RT |  | HT |  |
| Year Built | 1993 | Next Insp. |  | Insp. Type |  |
| Service | SWEET | Manway | N | Coating |  |
| PSV #. | CHN-001-341 |
| Mfg. | TAYLOR | Serial # | 47524-94 | Set Pressure | 1330 PSI |
| Type/Model | T-8200-1 | Capacity | 4789 SCFM | Size | 1 |
| Date of Service | 10/6/2009 | Next Service |  | Service Co. | IDEAL PRECISION VALVE |

Notes:										Report #

Completed by: Don Burren				Contact Number: 403-304-4951